RepRapPro inkjet – Instructions – General Notes

Principle
The HP51604A inkjet cartridge is a thermal inkjet, with 12 nozzles on the print head. Each nozzle has an accompanying 65 ohm resistor. The nozzles are small enough that the surface tension of the ink will prevent droplets flowing out under normal circumstances. When a voltage pulse is applied to a nozzle connection the resistor heats up, rapidly boiling a small amount of ink around the resistor. This bubble forces a small droplet of ink out of the nozzle.

Because the inkjet head has 12 nozzles, arranged in a line, an image can be produced 12 pixels at a time. Typical operation would sweep the print head along a line, firing nozzles as required to produce a line of the image, 12 pixels thick. The print head would then be moved down, and the next line drawn. This technique greatly decreases print time, compared to if only a single nozzle was used.

Pin Connections

Driver Electronics
The inkjet requires a supply voltage of around 20V. A typical circuit would have the common connection of the cartridge at 20V, and each nozzle line connected to an open drain FET. Pulsing the gate of the FET high will fire the nozzle. See figure for reference.

The nozzle resistors are very sensitive to the length of the voltage pulse used to trigger them. A pulse too short will not provide enough energy to boil the ink; too long and the resistor will be destroyed, rendering the associated nozzle useless. The recommended amount of energy in the pulse is 40μJ (40 microjoules).

The required pulse length can be calculated using the formula:
Pulse length = Resistance * Energy / (Voltage)^2

The table below lists pulse lengths at various supply voltages:

Voltage (V)	Pulse Length (μs
19	7.2
20	6.5
21	5.9
22	5.4
23	4.9
24	4.5

-Consider how your circuit behaves when reset or uploading to a microcontroller.

Operational notes